## Slide 1: Theoretical Modeling and Experimental Validation of Physiologically Relevant Flows and Their Applications
Committee Members:
Eugene R. Pawlak, Mechanical and Aerospace Engineering, co-chair
Antonio L. Sánchez, Mechanical and Aerospace Engineering, co-chair
Stephanie Lindsey, Mechanical and Aerospace Engineering
Mitsue Miyazaki, Radiology
David Saintillian, Mechanical and Aerospace Engineering
By Obed Armando Campos

## Slide 2: Outline
Introduction
Part 1: Engineering Physiologically Relevant Flow Environments for Pulmonary Arterial Endothelial Studies
  Chapter 1: A Multi-Chamber Pulsating-Flow Device with Optimized Spatial Shear Stress and Pressure for Endothelial-Cell Testing
  Chapter 2: Poiseuille Flow with a Stretching Bottom Wall
Part 2: Cerebrospinal Fluid (CSF) Transport and Noninvasive Flow Quantification
  Chapter 3: Phantom Based Evaluation of Time-SLIP MRI for Measuring Spinal-Canal Lagrangian Drift
1/40

## Slide 3
Cerebrospinal Fluid Flow in the Spinal Canal
Blood Flow in Main Pulmonary Artery
openart.ai
2/40

## Slide 4: Part 1: Engineering Physiologically Relevant Flow Environments for Pulmonary Arterial Endothelial Studies
3/40

## Slide 5: Background
Heart pumps blood through the body
  Contraction and relaxation of the heart leads to periodic fluctuations in the blood flow.
Endothelial cells that line the blood vessels can sense changes in flow through mechanical loads.
Section of Blood Vessel
Endothelium
FLOW
Endothelial Cells
Shear Stress
Pressure
(Normal Stress)
Stretching
~2.5cm
4/40

## Slide 6: Why Do We Care About MPA and PAECs?
Motivation:
Children with congenital heart disease can develop pulmonary hypertension (PH). Current pharmaceuticals do not offer longer term alleviation for PH.
Goal:
We can study pulmonary hypertension by looking at the genetic response of PAECS varying changes in flow shear stress, pressure and stretching. With hopes of developing better pharmaceuticals.
  With flow apparatus that apply these loads uniformly to large testing sample using a flow rate that idealizes main pulmonary artery flow.
5/40

## Slide 7: Chapter 1: A Multi-Chamber Pulsating-Flow Device with Optimized Spatial Shear Stress and Pressure for Endothelial-Cell Testing
6/40

## Slide 8: Our Focus
Q(t)
Top View
Coverslips
x
z
Testing
Region
We want to expedite experiments and maintain accuracy of applied forces to a large cell sample size.
Side View
7/40
Notes: Talk about cells being in the bottom

## Slide 9: Theoretical Model
Objective
Considerations
The relevant lubrication Reynolds number satisfies
where
Setup
y
z
8/40

## Slide 10
Dimensionless Variables
, ,
+
+
+
Governing Equations for 2D Unsteady Lubrication
=
Womersley Number
Boundary Conditions
Dimensionless Objective
Point Source
Top View
,
Point Sink
Dimensionless Governing Equations
9/40
Notes: We then dimensionless the problem using these dimensionless variables shown here.
Which lead us to our 2D unsteady lubrication governing eqautions, with the boundary conditions coming from no slip on the top and bottom plates. As well, as our dimensionless wall shear stress
Two important dimensionless parameters arise here, the womersely number M, wich describes the pulsating frequency in relation to the viscous effects and the aspect ratio lambda which I will become relevant later.
Further we only looking at half of the planform of the chamber due to symmetry.
As well, the inlets and outlets are described as point and sink sources that are placed at their respective lengthwise end corners.

## Slide 11
Flow Theory: 3D Model for PPFC
Spatial Component [Horizontal Structure ψ(x,y)]: Function of Λ.
Temporal Component: Function of on and .
Vertical Structure (
3D Solution:
Oh
10/40

## Slide 12
Temporal Fluctuations
(Shear Stress)
(Pressure)
(Flow Rate)
z
V(z)
11/40
Notes: Explain the axis and the plot contents

## Slide 13
Shear Stress Spatial Anomaly
12/40
Notes: This is normalize anomaly showing here for the shear stress metric

## Slide 14: MCS
Flow Output
to piston pump
Flow Input, Q(t), from piston pump
CAD Model of Mutiplex Cell Shearer
Side View of Perfusion Chamber
13/40
Notes: Add scaling here

## Slide 15: Experimental Setup for Particle Tracking Velocimetry (PTV)
Pump Input:
Single Perfusion Chamber
Camera
Arduino
Computer
Direction of Flow
Pressure Sensor
Ball Valve
Directional Valve
Contaminated Reservoir
Clean Water
Mixer with Particles
Pulsatile (Piston) Pump
14/40

## Slide 16: Flow with Tracer Particles
Testing Region
15/40
Notes: Let it run at least twice

## Slide 17: Streamlines
Testing Region
16/40
Notes: Go through this carefully

## Slide 18: Pressure Measurements
Q(t)
17/40

## Slide 19: Chapter 2: Poiseuille Flow with a Stretching Bottom Wall
18/40
Notes: Transition, take the pause, introduce how we are missing stretching

## Slide 20: Background
Heart pumps blood through the body
  Contraction and relaxation of the heart leads to periodic fluctuations in the blood flow.
Endothelial cells that line the blood vessels can sense changes in flow through mechanical loads.
Section of Blood Vessel
Endothelium
FLOW
Endothelial Cells
Shear Stress
Pressure
(Normal Stress)
Stretching
~2.5cm
4/40

## Slide 21
Stretching
19/40

## Slide 22
Analysis is similar as before
Linear
Lubrication problem due to Hele-Shaw cell
Transverse Flow: Leading Order
20/40
Moving lower boundary
Longitudinal flow is uncoupled
Notes: Longitudinal flow is unchanged, if it was infinitely long channel they are uncoupled

## Slide 23
Membrane Holder on Motor
Membrane Through Device
Orthogonal View
Transverse of Flow Slice View
Rollers
Motors with Membrane Holder
Tank
Flow Chamber
with Membrane
21/40

## Slide 24
Flow Chamber
Membrane
Drain
Pump
Dye
Camera
Tank
Flow Meter
22/40

## Slide 25
Upper Dye
Lower Dye
Together
23/40

## Slide 26
Reference
Upper Dye
Lower Dye
For a Single Frame
100 mm
Single Cycle
a)
b)
24/40
Notes: Add summary of the results

## Slide 27: Part 2: Cerebrospinal Fluid (CSF) Transport and Noninvasive Flow Quantification
25/40

## Slide 28: Introduction
Cerebrospinal Fluid (CSF)
The entire surface of central nervous system is bathed by a clear, colorless fluid called cerebrospinal fluid (CSF).
Properties:
CSF is a Newtonian fluid,
Viscosity and density at 37 C° water
A human adult has about 140-170 ml of CSF:
  30 ml are in the ventricles,
  70-80 ml in the cerebral SAS
  50 ml in the spinal SAS.
26/40
Notes: Shock Absorber that protects brain tissue.
Regulates distribution of substances, removes metabolic waste, and maintains Intracranial Pressure (ICP).

## Slide 29: Chapter 3: Phantom Based Evaluation of Time-SLIP MRI for Measuring Spinal-Canal Lagrangian Drift
27/40

## Slide 30: Intrathecal Drug Delivery
Injection of drugs into the subarachnoid space
Injection methods:
Single dose
Continuous infusion
Target locations:
Brain (chemotherapy)
Spine (spinal anesthesia)
Drug diffusivity:
Schmidt number:
Drug density:
CSF Density:
28/40

## Slide 31: Motion in the Spinal Canal
Fast oscillatory motion
Slow drift
Driven by cardiac and respiratory cycles
~ 2 cm/min
~ 30 min
Need a non-invasive method to measure Lagrangian drift
~ 5 cm/s
~ 1 s
cm/s
Patient specific drug dispersion predictions
T sec
Notes: Diffusivity is so small

## Slide 32
0.2 cm
(canal width)
3 cm
(spinal cord perimeter)
Spinal Canal Phantom
Flow
Compliant Exterior
Thickness 8mm
Interior Diameter 2.1 cm
Rigid Rod
Diameter of 1 cm
Entrance
Closed End
30/40
Notes: Objective to develop methodology,

## Slide 33: Theoretical CSF Motion Model
Asymptotic expansions for :
Leading-order solution:
First-order corrections:
Oscillation time:
1 s
Mean Lagrangian drift:
30 min
Mean Lagrangian Velocity
Steady Streaming
Lagrangian
Drift
neglected and terms
Momentum balance
J. J. Lawrence, et al, J. Fluid Mech., 861 679-720 (2019)
31/40
Notes: Cite theory

## Slide 34
Theoretical Predictions: Slow Drift
Phantom has constant and
Predictions are dependent on the eccentricity and Womersley Number
Javier Alaminos-Quesada
32/40
Notes: Cite theory

## Slide 35
Non-Invasive Measurements: Setup
Piston Pump
(Vivitro Labs)
Pump Input
MRI Room
33/40

## Slide 36
Phase Contrast to capture slow drift ?
34/40
Notes: Pc gives us mean eulerian velocity
Spatial and temporal accuracy is not enough

## Slide 37
35/40
Notes: Explain why would wait longer,

## Slide 38
How Do We Get a Profile?
36/40

## Slide 39
Qualitative Results
37/40
Notes: Add a circle to highlight the discrepancies

## Slide 40
Displacement Results
38/40

## Slide 41: Acknowledgements
Committee
  Dr. Geno Pawlak,
  Dr. Antonio Sanchez
  Dr. Stephanie Lindsey
  Dr. Mitsue Miyazaki
  Dr. David Saintillian
Family
  Angel Flores
  Esther Campos
  Eva Campos
  Mario Flores
  Eli Alfaro
Facilities and Staff
  MAE Machine Shop
  MAE Design Studio
  Thomas Chalfant
  Steve Mercask
  Akemi Alpaslan
  Chris Cassidy
Collaborators
  Pawlak Lab
  Sanchez Lab
  Lindsey Lab
  Wilfred Conen
  Stephanie Sincomb
  Javier Alaminos Quesada
  Vadim Malis Candido Gutierrez Montes
  Carlos Martinez Bazan
  Amy Shwartz
39/40

## Slide 42: Thank You!
40/40